## Slide 1
Leif Bloomquist
Rethinking Art and the Machine
Tools For 8 Bit Music
@ THEMUSEUM – Kitchener, ON, Canada
December 11, 2011

## Slide 2: Project Goals
Make the Commodore VIC-I (6560) chip’s distinctive sound available to electronic musicians.
Easy integration with sequencers, synthesizers, or tracking software using MIDI1.
1Musical Instrument Digital Interface

## Slide 3: The VIC-20’s Voices
Square Wave output (except Noise)
Some overlap between voices

## Slide 4: The MIDI Protocol
Defined in 1982.
Asynchronous Serial Interface at 31.25 Kbps.
Messages consist of a Status byte (bit #7 set) followed by Data bytes (usually two).
16 “Channels”.
Commands such as Note On, Note Off, Control Change, etc.

## Slide 5: Typical MIDI Message
9 | 1 | 3C | 40
Status
byte
Data
bytes
Channel
Command

## Slide 6: Hardware Schematic
From Electronics, the Maplin Magazine
http://members.lycos.co.uk/templarseries/maplin.html

## Slide 7: Prototype

## Slide 8: Software
6502 Assembler
Cross-compiled using DASM2
2 http://dasm-dillon.sourceforge.net/

## Slide 9: Implementation
One MIDI Channel per Voice
    Channel 1 = Alto (36874)
    Channel 2 = Tenor (36875)
    Channel 3 = Soprano (36876)
    Channel 4 = Noise (36877)
Master Volume is set through Controller #7 (Coarse Volume) on any channel

## Slide 10: Implementation (Continued)
Note On commands use a lookup table to match MIDI Note# to the closest match for that voice.
Controller #1 (Course Modulation) does a direct “POKE” to the corresponding Voice register.
Note Off, All Notes Off commands on a specific channel are used to silence that voice.

## Slide 11: Left to Implement
MIDI “Running Status”
MIDI-Out (use the VIC keyboard to control external hardware)
Mono/Polyphony Modes that use multiple voices
PAL or NTSC lookup tables
Viznut’s waveforms

## Slide 12: Next Steps
More sophisticated prototype including MIDI Out and autostart ROM
Small manufacturing run of cartridges – quantity and price TBD.

## Slide 13: Credits
Hardware:
    LD. Ball
    Francois Leveille
    Jim Brain
Software:
    Leif Bloomquist
    David Viens
    “Viznut”

## Slide 14: Demo Tune!
http://soundcloud.com/schema-factor/rethinking-art-and-the-machine